Applied Geometry
and
special effects
2010
By Pål Trefall

---
Introduction
- Architecture
- Curves
- Triangulation
- Quad-tree
- Project
- Demo

---
Architecture
- Modular
  - Component-driven Objects, build objects from pieces of logic (aggregation) instead of inheritance.
- Data-driven
  - Script
    - Define components in Lua script
      - Curve evaluation components, special effects components, etc.
    - C++ engine exposure via intuitive syntax
    - Scene initialization definition
  - XML
    - Define entities
      - Aggregation of components
      - Set initial property values
    - Engine configuration

---
Architecture
- Multi-threaded curve evaluation
  - Parametric curve points are independent
  - Potentially millions of points on curve to evaluate
  - Spawn worker-thread pool equal to number of cores
  - Each evaluation is a job on a job-queue
  - Workers pop jobs from queue
  - Evaluate curve in parallel

---
Curves
- B-Spline
  - n+1 control points cpts
  - Degree d
  - n+d+2 knots
  - t is the interpolated parametric value between start and end of the paramertric interval (the curve).
  - Generate Bernstein-Hermite matrix, BHM, that holds the polynomials based on t.
  - The pointset p is the point on the curve at t and all its derivatives.
  - We find p on the B-Spline curve by using the BHM to weight the cpts

---
Curves
- Expo-Rational B-Spline (ERBS)
  - C∞-Smooth (can never derivate to 0)
  - Construction
    - Define number of local curves, nlc, and the degree of the polynomials d
    - Look at nlc number of points, pi, on input curve and the d-1 derivatives of each pi to define the local pointset p.
    - For each p, we multiply by the inverse Bernstein-Hermite matrix to find the control-points, cpts, for each local curve of the ERBS.
  - Evaluate curve by blending two local curves for each pointset based on the t interval

---
Quad-tree evaluation
- Organization of data in quadrants
- Can be used to, for example, look up a specific pixel in a 2D image
- Each node in tree represent a region
- Split when maximum capacity of region is reached
- Splits in four children at each level of the Quad-tree
- Steiner product

---
Triangulation
- Delaunay
  - Triangulates a set of points
  - Must adher to the Delaunay condition
    - The circle x through abc can not contain any points
    - If sum of the angle of the adjacent point in the new triangle is lequal to 180 degrees.
    - FLIP

---
Project
- Input curve of ERBS specified via lua script component
  - Rose, Butterfly, Spiral
- Special effects written in lua script component
- Curves defined in XML
- Scene defined in Script
- Curve, Bezier and ERBS PCurve objects defined in C++, and inherits from Ientity
- Very easy to define new input curves in script
- Very easy to add new special effects in script
- Little to no recompilation of code required to expand project!

---
DEMO